## Slide 1
  Avoiding, Hiding and Managing Communication at the Exasacle
Kathy Yelick
Associate Laboratory Director
Computing Sciences
Lawrence Berkeley National Lab
Professor of Electrical Engineering
and Computer Sciences
UC Berkeley

## Slide 2: Science at the Boundary of Simulation and Observation
Cosmology
Environment
Materials
In many areas, there are opportunities to combine simulation and observation for new discoveries.
These will require increased computing capabilities.

## Slide 3: Hardware Trend: More Parallelism at Lower Levels
Chart: 
| 1990.0 | 1995.0 | 2000.0 | 2005.0 | 2010.0 | 2015.0 | 2020.0
 | 450000000 | 1000000000 | 6000000000 | 14000000000 | 111000000000 | 1200000000000 | 11400000000000 | 107000000000000 | 207000000000000 | 103900000000000 | 1352000000000000 | 2330000000000000 | 2330000000000000 | 3080000000000000
 | 900000000 | 1710000000 | 3249000000 | 6173100000 | 11728890000 | 22284891000 | 42341292900 | 80448456510 | 152852067369 | 290418928001.1 | 551795963202.09 | 1.0484e+12 | 1.992e+12 | 3.7848e+12 | 7.1911e+12 | 1.3663e+13 | 2.596e+13 | 4.9323e+13 | 9.3715e+13 | 178057769009428 | 338309761117913 | 642788546124036 | 1221298237635670 | 2320466651507770 | 4408886637864760 | 8376884611943040 | 15916080762691800 | 30240553449114400 | 57457051553317296 | 1.0917e+17 | 2.0742e+17 | 3.941e+17 | 7.4879e+17 | 1.4227e+18
  Application Performance Growth
  (Gordon Bell Prizes)
Vector parallelism
Manycore Parallelism
More, slower cores
Multicore parallelism
ILP,
TLP
More, slower devices; new levels of parallelism

## Slide 4: Data Movement is Expensive
CPU cycle time vs memory access time
Sources: http://csapp.cs.cmu.edu/2e/figures.html, http://csapp.cs.cmu.edu/3e/figures.html
Chart: Year
| 1980.0 | 1985.0 | 1990.0 | 1995.0 | 2000.0 | 2003.0 | 2005.0 | 2010.0 | 2015.0
Disk seek time | 87000000 | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
Flash SSD access time | 75000 | 50000
DRAM access time | 375 | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 300 | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 1000 | 166 | 50 | 6 | 1.6 | 0.3 | 0.25 | 0.1 | 0.08
CPU
SRAM
DRAM
SSD
Disk

## Slide 5: Data Movement is Expensive
Source: http://slideplayer.com/slide/7541288/
120 pJ
2000 pJ
250 pJ
~2500 pJ
100 pJ
6 pJ
Cost to move data off chip to a neighboring node
Cost to move data off chip into DRAM
Cost to move off-chip, but stay within the package (SMP)
Cost to move data 20 mm on chip
Typical cost of a single floating point operation
Cost to move data 1 mm on-chip
Hierarchical energy costs.
Notes: From: OpenSoC Fabric slides. Farzad Fatollahi-Fard

## Slide 6: Summary
More parallelism
Diversity of processors / accelerators
Communication (data movement) is expensive

## Slide 7: Compilers and Autotuning

## Slide 8: Autotuning: Write Code Generators
Two “unsolved” compiler problems:
  dependence analysis and
  accurate performance models
Autotuners are code generators plus search
Work by Williams, Oliker, Shalf, Madduri, Kamil, Im, Ethier,…
512
256
128
64
32
16
8
4
2
1024
1/16
1
2
4
8
16
32
1/8
1/4
1/2
1/32
512
256
128
64
32
16
8
4
2
1024
1/16
1
2
4
8
16
32
1/8
1/4
1/2
1/32
single-precision peak
double-precision peak
single-precision peak
double-precision peak
STREAM bandwidth
Device bandwidth
RTM/wave eqn.
RTM/wave eqn.
7pt Stencil
27pt Stencil
Xeon X5550 (Nehalem)
NVIDIA C2050 (Fermi)
DP add-only
DP add-only
SpMV
SpMV
7pt Stencil
27pt Stencil
DGEMM
DGEMM
GTC/chargei
GTC/pushi
GTC/chargei
GTC/pushi
Gflop/s
Algorithmic intensity: Flops/Word
Algorithmic intensity: Flops/Word
Gflop/s
Autotuning avoids this problem
Domain-Specific Languages help with this
✔

## Slide 9: Libraries vs. DSLs (domain-specific languages)
Chart: 
| Adaptive | Dense LA | Monte Carlo | Particles | Spectral | Sparse LA | Structured
 | 0.14625 | 0.20638 | 0.22595 | 0.24922 | 0.34319 | 0.35965 | 0.38917
Dense Linear Algebra | Atlas
Spectral Algorithms | FFTW, Spiral
Sparse Linear Algebra | OSKI
Structured Grids | TBD
Unstructured Grids | 
Particle Methods | 
Monte Carlo | 
NERSC survey: what motifs do they use?
What code generators do we have?
Unstructured
Stencils are both the most important motifs and a gap in our tools

## Slide 10: Approach: Small Compiler for Small Language
Snowflake: A DSL for Science Stencils
  Domain calculus inspired by Titanium, UPC++, and AMR in general
Complex stencils: red/black, asymmetric
Update-in-place while preserving provable parallelism
Complex boundary conditions

## Slide 11: Snowflake Performance
Performance on the HPGMG application benchmark using all the features of Snowflake
Competitive with hand-optimized performance
Within 2x of optimal roofline
Nathan Zhang, C. Markley, S. Williams, A. Fox, K. Yelick

## Slide 12: DSLs popular outside scientific computing
Developed for Image Processing
  10+ FTEs developing Halide
  50+ FTEs use it; > 20 kLOC
HPGMG (Multigrid on Halide)
Halide Algorithm by domain expert
Halide Schedule either
  Auto-generated by autotuning with opentuner
  Or hand created by an optimization expert
Halide performance
Autogenerated schedule for CPU
Hand created schedule for GPU
No change to the algorithm
Func Ax_n("Ax_n"), lambda("lambda"), chebyshev("chebyshev");
Var i("i"),j("j"),k("k");
Ax_n(i,j,k) = a*alpha(i,j,k)*x_n(i,j,k) - b*h2inv*(
beta_i(i,j,k) *(valid(i-1,j,k)*(x_n(i,j,k) + x_n(i-1,j,k)) - 2.0f*x_n(i,j,k))
+ beta_j(i,j,k) *(valid(i,j-1,k)*(x_n(i,j,k) + x_n(i,j-1,k)) - 2.0f*x_n(i,j,k))
+ beta_k(i,j,k) *(valid(i,j,k-1)*(x_n(i,j,k) + x_n(i,j,k-1)) - 2.0f*x_n(i,j,k))
+ beta_i(i+1,j,k)*(valid(i+1,j,k)*(x_n(i,j,k) + x_n(i+1,j,k)) - 2.0f*x_n(i,j,k))
+ beta_j(i,j+1,k)*(valid(i,j+1,k)*(x_n(i,j,k) + x_n(i,j+1,k)) - 2.0f*x_n(i,j,k))
+ beta_k(i,j,k+1)*(valid(i,j,k+1)*(x_n(i,j,k) + x_n(i,j,k+1)) - 2.0f*x_n(i,j,k)));
lambda(i,j,k) = 1.0f / (a*alpha(i,j,k) - b*h2inv*(
beta_i(i,j,k) *(valid(i-1,j,k) - 2.0f)
+ beta_j(i,j,k) *(valid(i,j-1,k) - 2.0f)
+ beta_k(i,j,k) *(valid(i,j,k-1) - 2.0f)
+ beta_i(i+1,j,k)*(valid(i+1,j,k) - 2.0f)
+ beta_j(i,j+1,k)*(valid(i,j+1,k) - 2.0f)
+ beta_k(i,j,k+1)*(valid(i,j,k+1) - 2.0f)));
chebyshev(i,j,k) = x_n(i,j,k) + c1*(x_n(i,j,k)-x_nm1(i,j,k))+
c2*lambda(i,j,k)*(rhs(i,j,k)-Ax_n(i,j,k));
Chart: Execution Time
| Original | Halide CPU | Halide GPU
256^3 | 0.96254 | 0.85935 | 0.64119
128^3 | 0.28738 | 0.21513 | 0.17673
64^3 | 0.086662 | 0.056151 | 0.050216
32^3 | 0.043272 | 0.020197 | 0.015759
16^3 | 0.039127 | 0.003395 | 0.003461
8^3 | 0.04545 | 0.000674 | 0.000671
4^3 | 0.049371 | 0.000151 | 0.000345
2^3 | 0.051585 | 9.4e-05 | 0.005805
1^3 | 0 | 0 | 0
g+
Image
Auto
Enhance

## Slide 13: Algorithms for the Hardware

## Slide 14: Beyond Domain Decomposition 2.5D Matrix Multiply on BG/P, 16K nodes / 64K cores
c = 16 copies
EuroPar’11 (Solomonik, Demmel)
SC’11 paper (Solomonik, Bhatele, Demmel)
Surprises:
Even Matrix Multiply had room for improvement
Idea: make copies of C matrix (as in prior 3D algorithm, but not as many)
Result is provably optimal in communication
Lesson: Never waste fast memory
And don’t get hung up on the owner computes rule
Can we generalize for compiler writers?
Notes: SC’11 paper about need to fully utilize 3D torus network on BG/P to get this to work

## Slide 15: Deconstructing 2.5D Matrix Multiply Solomonick & Demmel
x
z
z
y
x
y
Tiling the iteration space
2D algorithm: never chop k dim
2.5 or 3D: Assume + is associative; chop k, which is  replication of C matrix
k
j
i
Matrix Multiplication code has a 3D iteration space
Each point in the space is a constant computation (*/+)
for i
for j
for k
B[k,j] …
A[i,k] …
C[i,j] …

## Slide 16: Using .5D ideas on N-body
n particles, k-way interaction.
  Molecules, stars in galaxies, etc.
Most common: 2-way N-body
Best algorithm is to divide n particles into p groups??
for t timesteps
forall i1, …, ik
force[i1] += interact(particle[i1], …, particle[ik])
forall i
move(particle[i], force[i])
.......................................................................................
O(nk).
No!

## Slide 17: Communication Avoiding 2-way N-body (using a “1.5D” decomposition)
Divide p into c groups
Replicate particles across groups
Repeat: shift copy of n/(p*c) particles to the left within a group
Reduce across c to produce final value for each particle
  Total Communication: O(log(p/c) + log c) messages,
  O(n*(c/p+1/c)) words
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
............
c
p/c
Driscoll, Georganas, Koanantakool, Solomonik, Yelick

## Slide 18: Less Communication..
Cray XE-6; n=24K particles, p=6K cores
Down is good
96% reduction in shift time (red)
Notes: = 78.38
√𝒑 = 78.38

## Slide 19: Strong Scaling
4.4x
Up is good

## Slide 20: Challenge: Symmetry & Load Balance
Force symmetry (fij = -fji) saves computation
2-body force matrix vs 3-body force cube
How to divide work equally?
6x save
of O(n3)!
2x save
of O(n2)

## Slide 21: 3-Way N-Body Speedup
Down is good
Cray XC30, 24k cores, 24k particles
22.1x
Koanantakool & Yelick
Notes: C=64
22.13x speedup
99.95% reduction in communication time

## Slide 22: Perfect Strong Scaling
Up is good
42x
BlueGene/Q 16k particles, Strong Scaling
Koanantakool & Yelick

## Slide 23: Sparse-Dense Matrix Multiply Too!
Variety of algorithms that divide in or 2 dimensions
Koanantakool & Yelick

## Slide 24: 100x Improvement
A66k x 172k, B172k x 66k, 0.0038% nnz, Cray XC30
100x
Up is good
Koanantakool & Yelick
Notes: Stochastic linear programming problem

## Slide 25: Linear Algebra is important to Machine Learning too!
Dense Matrix Vector
(BLAS2)
Sparse - Sparse Matrix Product
(SpGEMM)
Sparse Matrix Times Multiple Dense Vectors
(SpMM)
Sparse Matrix-Dense Vector (SpMV)
Sparse Matrix-Sparse Vector (SpMSpV)
Increasing arithmetic intensity
Graphical Model Structure Learning (e.g., CONCORD)
Clustering (e.g., MCL, Spectral Clustering)
Logistic Regression, Support Vector Machines
Dimensionality Reduction (e.g., NMF, CX/CUR, PCA)
Deep Learning (Convolutional Neural Nets)
Sparse - Dense Matrix Product
(SpDM3)
Dense Matrix Matrix (BLAS3)
Aydin Buluc, Sang Oh, John Gilbert, Kathy Yelick

## Slide 26: Overhead Can’t be Tolerated

## Slide 27: PGAS: A programming model for exascale
Global address space: thread may directly read/write remote data using an address (pointers and arrays)
  … = *gp; ga[i] = …
Partitioned: data is designated as local or global
shared int [ ] ga; and upc_malloc (…)
Global address space
x: 1
y:
l:
l:
l:
g:
g:
g:
x: 5
y:
x: 7
y: 0
p0
p1
pn
A programming model can influence how programmers think
Examples:
UPC
UPC++

## Slide 28: One-Sided Communication is Closer to Hardware
Hardware does 1-sided communication
Overhead for send/receive messaging is worse at exascale
message ID
address
data payload
data payload
two-sided put message
one-sided message
network
interface
memory
host
CPU
Chart: 
| isend (off) | irecv (off) | isend (on) | irecv (on)
Nanoseconds for Edison | 1538.3333 | 480.8333 | 525.8333 | 801.6667
Nanoseconds
Software Overhead
Chart: 
| isend (off) | irecv (off) | isend (on) | irecv (on)
Nanoseconds for Edison | 1538.3333 | 480.8333 | 525.8333 | 801.6667
Chart: 
| isend (off) | irecv (off) | isend (on) | irecv (on)
Nanoseconds for Edison | 1538.3333 | 480.8333 | 525.8333 | 801.6667
Nanoseconds for 1GHz x86 | 3692 | 1154 | 1262 | 1924
Chart: 
| isend (off) | irecv (off) | isend (on) | irecv (on)
Nanoseconds for Edison | 1538.3333 | 480.8333 | 525.8333 | 801.6667
Nanoseconds for 1GHz x86 | 3692 | 1154 | 1262 | 1924
Chart: 
| isend (off) | irecv (off) | isend (on) | irecv (on)
Nanoseconds for Edison | 1538.3333 | 480.8333 | 525.8333 | 801.6667
Nanoseconds for 1GHz x86 | 3692 | 1154 | 1262 | 1924
Nanoseconds for 1GHz SIMT? | 29536 | 9232 | 10096 | 15392
2.9 GHz x86
1 GHz x86 (model)
1 GHz 3-SIMT (model)

## Slide 29: One-sided PGAS (UPC++) in AMR
Adaptive Mesh Refinement (AMR) using UPC++
  Metadata costs make flat MPI impractical
  Replaced communication (retained most code)
  Hierarchical algorithms (UPC++/UPC++ or MPI/MPI best)
Weiquin Zhang, Y. Zheng

## Slide 30: Avoid Unnecessary Synchronization

## Slide 31: Sources of Unnecessary Synchronization
Libraries
Abstraction
Loop Parallelism
Accelerator Offload
Bulk Synchronous
Less Synchronous
!$OMP PARALLEL DO
DO I=2,N
B(I) = (A(I) + A(I-1)) / 2.0
ENDDO
!$OMP END PARALLEL DO
Analysis | % barriers | Speedup
Auto | 42% | 13%
Guided | 63% | 14%
NWChem: most of barriers are unnecessary (Corvette)
LAPACK: removing barriers ~2x faster (PLASMA)
“Simple” OpenMP parallelism implicitly synchronized between loops
The transfer between host and GPU can be slow and cumbersome, and may (if not careful) get synchronized

## Slide 32: Asynchronous Sparse Cholesky in UPC++
Fan-both algorithm by Jacquelin & Ng, in UPC++

## Slide 33: Whole-Mantle Seismic Model Using UPC++
First-ever whole-mantle seismic model from numerical waveform tomography
Finding: Most volcanic hotspots are linked to two spots on the boundary between the metal core and rocky mantle 1,800 miles below Earth's surface.
Scott French, Barbara Romanowicz, "Broad plumes rooted at the base of the Earth’s mantle beneath major hotspots", Nature, 2015
Makss unsolvable problems solvable!
Notes: Additional paper: Scott French, Barbara Romanowicz, "Whole-mantle radially anisotropic shear velocity structure from spectral-element waveform tomography", Geophysical Journal International, 2014, 199, doi: 10.1093/gji/ggu334

## Slide 34: Data Fusion for Observation with Simulation
Unaligned data from observation
One-sided strided updates
Could MPI-3.0 one-sided do this? Yes, but not well so far
Scott French, Y. Zheng, B. Romanowicz, K. Yelick

## Slide 35: Unstructured, Graph-based, Data analytics problem: De novo Genome Assembly
DNA sequence consists of 4 bases: A/C/G/T
Read: short fragment of DNA sequence that can be read by a DNA sequencing technology – can’t read whole DNA at once.
De novo genome assembly: Reconstruct an unknown genome from a collection of short reads.
  Constructing a jigsaw puzzle without having the picture on the box
Notes: First I’ll present some definitions relevant to the problem

## Slide 36: Strong scaling (human genome) on Cray XC30
Complete assembly of human genome in 4 minutes using 23K cores.
700x speedup over original Meraculous (took 2,880 minutes on large shared memory with some Perl code); Some problems (wheat, squid, only run on HipMer version)
Makes unsolvable problems solvable!

## Slide 37: Summary
Communication is the most expensive thing computers do
  Memory
  Network
Compilers
  Domain specific languages simplify program analysis
  Autotuning helps identify optimizations
PGAS and one-sided communication can help lower costs
  Better match to RDMA hardware
  Also supports applications with irregular accesses
Algorithms can avoid communication
  Both data volume (bandwidth) and number of messages (latency)
  Probably optimal and faster (more scalable) in practice

## Slide 38
  Thank you!
Notes: I will be discussing our Exascale Science strategy, and then introduce the talks for the rest of the exascale section.